Sure Klean® Liquid Marble Cleaner Specification

Specifier Note:  The information provided below is intended to guide the Architect in developing specifications for products manufactured by PROSOCO, Inc. and should not be viewed as a complete source of information about the product(s).  The Architect should always refer to the Product Data Sheet and MSDS for additional recommendations and for safety information.

Specifier Note:  Paragraph below is for PART 1 GENERAL, Quality Assurance.

# Test Area

Test a minimum 4 ft. by 4 ft. area on each type of masonry. Use the manufacturer’s application instructions. Let test area protective treatment cure before inspection. Keep test panels available for comparison throughout the cleaning project.

Specifier Note:  Paragraphs below are for PART 2 PRODUCTS, Manufacturers and Products.

# Manufacturer

PROSOCO, Inc., 3741 Greenway Circle, Lawrence, KS 66046.  Phone: (800) 255-4255; Fax: (785) 830-9797.  E-mail:  CustomerCare@prosoco.com

# Product Description

Sure Klean® Liquid Marble Cleaner is a non-acidic, phosphate-free, low-odor, orange-colored gel designed for the cleaning, restoration and maintenance of polished stonework or glazed masonry. Liquid Marble Cleaner loosens and dissolves surface dirt, carbon buildup and other atmospheric stains, allowing them to be washed away with a simple water rinse.

# Typical Technical Data

FORM: orange gel

SPECIFIC GRAVITY: 1.13

pH: 12.0

WEIGHT/GALLON: 9.4 pounds

ACTIVE CONTENT: not applicable

TOTAL SOLIDS: not applicable

FLASH POINT: grater than 212 degrees Fahrenheit (greater than 100 degrees Celsius) ASTM D 3278

FREEZE POINT: 32 degrees Fahrenheit (0 degrees Celsius)

SHELF LIFE: 2 years in tightly sealed, unopened container

VOC CONTENT: less than 0.1 percent

# Limitations

- May dull or remove waxes or other applied finishes.

- Repeated use may dull polished stonework.

Specifier Note:  Paragraphs below are for PART 3 EXECUTION, Installation.

# Application

Before applying, read “Preparation” and “Application” sections in the Manufacturer’s Product Data Sheet for Liquid Marble Cleaner.  Refer to the Product Data Sheet for additional information about product application and dilution.

Specifier Note: Do not atomize during application.

Application Instructions

- Liberally apply cleaner to the surface using a soft-bristled brush.

- Leave the cleaner on the surface for 15 to 20 minutes. Do not let the cleaner dry on the surface.

- Rinse the surface thoroughly with fresh water using sponges, brush and bucket, or low-pressure rinsing.

SPECIFIER NOTE: Change rinse water frequently. Thorough rinsing is extremely important to ensure all residues are removed from the surface.

# Cleanup

Clean tools and equipment immediately with soap and water.